## Slide 1
United States Environmental Protection Agency
Office of Water (4606)
EPA 816-F-01-003
June 2001
Radionuclides Rule:
A Quick Reference Guide
O v e r v i e w o f t h e R u l e | 
Title | Radionuclides Rule 66 FR 76708 December 7, 2000 Vol. 65, No. 236
Purpose | Reducing the exposure to radionuclides in drinking water will reduce the risk of cancer. This rule will also improve public health protection by reducing exposure to all radionuclides.
General Description | The rule retains the existing MCLs for combined radium-226 and radium-228, gross alpha particle radioactivity, and beta particle and photon activity. The rule regulates uranium for the first time.
Utilities Covered | Community water systems, all size categories.
P u b l i c H e a l t h B e n e f i t s | 
Implementation of | Reduced uranium
the Radionuclides | exposure for 620,000
Rule will result in . . . | persons, protection from
 | toxic kidney effects of
 | uranium, and a reduced
 | risk of cancer.
Estimated impacts of the Radionuclides Rule include . . . | Annual compliance costs of $81 million. On ly 795 systems will have to install treatment.
Cr i t i c a l D e a d l i n e s & R e q u i r e m e n t s | 
For Drinking Water Systems | 
June 2000 - December 8, 2003 | When allowed by the State, data collected between these dates may be eligible for use as grandfathered data (excluding beta particle and photon emitters).
December 8, 2003 | Systems begin initial monitoring under State-specified monitoring plan unless the State permits use of grandfathered data.
December 31, 2007 | All systems must complete initial monitoring.
For States | 
December 2000 - December 2003 | States work with systems to establish monitoring schedules.
December 8, 2000 | States should begin to update vulnerability assessments for beta photon and particle emitters and notify systems of monitoring requirements.
Spring 2001 | EPA meets and works with States to explain new rules and requirements and to initiate adoption and implementation activities.
December 8, 2002 | State submits primacy revision application to EPA. (EPA approves within 90 days.)
Regulated Contaminants |  | 
Regulated Radionuclide | MCL | MCLG
Beta/photon emitters* | 4 mrem/yr | 0
Gross alpha particle | 15 pCi/L | 0
Combined radium- 226/228 | 5 pCi/L | 0
Uranium | 30 µg/L | 0
*A total of 168 individual beta particle and photon emitters may be used to calculate compliance with the MCL. |  | 

## Slide 2
Initial Monitoring Results
MCL
< Detection Limit
Detection Limit but  1/2 the MCL
1/2 the MCL but < the MCL
First Compliance Cycle
2008 2009 2010 2011 2012 2013 2014 2015 2016
KEY
One sampling event.
4 consecutive quarterly samples. Systems with MCL violations must continue to take quarterly samples until 4 consecutive samples are at or below the MCL.
When allowed by the State, data collected between 6/00 and 12/08/03 may be used as grandfathered data to satisfy the initial monitoring requirements.
Final Rule 12/07/00
Initial Monitoring Begins unless State Permits the Use of Grandfathered Data
Grandfathered Data Initial Compliance Collected between Monitoring
06/00 12/08/03 2004 2005 2006 2007
Initial Monitoring Completed 12/31/07
For additional information on the Radionuclides Rule
Call the Safe Drinking Water Hotline at 1-800-426-4791; visit the EPA Web site at www.epa.gov/safewater; or contact your State drinking water representative. EPA will provide radionuclide training over the next year.
Applicability of the Standardized Monitoring Framework to Radionuclides
(Excluding the Beta Particle and Photon Emitters)
M o n i t o r i n g R e q u i r e m e n t s | 
Gross Alpha, Combined Radium-226/228, and Uranium (1) | Beta Particle and Photon Radioactivity (1)
Initial Monitoring | 
Four consecutive quarters of monitoring. | No monitoring required for most CWSs. Vulnerable CWSs (2) must sample for: Gross beta: quarterly samples. Tritium and Strontium-90: annual samples.
Reduced Monitoring | 
If the average of the initial monitoring results for each contaminant is below the detection limit: One sample every 9 years. If the average of the initial monitoring results for each contaminant is greater than or equal to the detection limit, but less than or equal to one-half the MCL: One sample every 6 years. If the average of the initial monitoring results for each contaminant is greater than one-half the MCL, but less than or equal to the MCL: One sample every 3 years. | If the running annual average of the gross beta particle activity minus the naturally occurring potassium-40 activity is less than or equal to 50 pCi/L: One sample every 3 years.
Increased Monitoring | 
A system with an entry point result above the MCL must return to quarterly sampling until 4 consecutive quarterly samples are below the MCL. | If gross beta particle activity minus the naturally occurring potassium-40 activity exceeds 50 pCi/L, the system must: Speciate as required by the State. Sample at the initial monitoring frequency.
All samples must be collected at each entry point to the distribution system. The rule also contains requirements for CWSs using waters contaminated by effluents from nuclear facilities. | 
G r a n d f a t h e r i n g o f D a t a | 
When allowed by the State, data collected between June, 2000 and December 8, 2003 may be used to satisfy the initial monitoring requirements if samples have been collected from: Each entry point to the distribution system (EPTDS). The distribution system, provided the system has a single EPTDS. The distribution system, provided the State makes a written justification explaining why the sample is representative of all EPTDS. | 
pscearce
2003-01-07 22:31:33
--------------------------------------------
<
pscearce
2003-01-07 22:34:47
--------------------------------------------
>